Simulation
With a joystick (keyboard) the user simulates the robot motion
Obtain information about velocities
Compute the input ensuring the velocity
Compute and update the generalized coordinates with the function PerformMotion
Compute the odometry
Prepare all the topic to be published and publish them

---
Feature and characteristic
Versatility:
All the characteristics of the robot, of the sensors, of the world are passed as	parameters so they can be changed:
Robot: max value of omega, wheel radius, front axle, joint offset (a in table), castor arm length (d in table), initial position
World: Xspacing, Yspacing, Linetickness
Sensor: position (x, y) in robot frame, world
Robot model built with URDF using xacro

---
Robot Component

---
Library
Eigen has everything we need:
Easy intuitive initialization
All the operations
Intuitive and semantic

---
Testing
Alpha testing: ok
Beta testing: if you want
Acceptance testing: if you think we should (UNIGE, CORO)

---
Sensor
Check the lines around it
Check different instances for the world (abort)
Different lines? No problem

---
Ground Generator
Different lines? No problem.
Further application: always generate ground under the robot

---
File Handler
Use rosbag and rosparam (safety)
Only one run
Check existence (add suffix)
Folder not found (create it)
Wrong path (abort)

---
Further Applications
New sensor: just define it
New world: just define it (modify generator accordingly)
New robot type? Why not?!